CS 475 Parallel Computing
Instructor: Matthew Meyn
Student: Khuong Luu (luukh)

Project 3

1. Tell what machine you ran this on
The computer I ran this experiment on has:
- Processor: Intel(R) Core(TM) i7-7700HQ CPU @ 2.80GHz
- Memory: 16GB, 2400Mhz
- Operating System: Ubuntu 16.04
- Kernel: 4.13.0-37-generic
- Number of Cores: 4
- Cache line size: 64 bytes
- Compiler: gcc version 5.4.0 20160609, OpenMP 3.1

2. Results

Performance unit is in Speed-up ratio (Compared to unparalleled version)
Padding Size unit is in 4 bytes (a size of a float)

3. Graph

Speed-up vs. Padding Size
Padding Size (in number of float size, or 4 bytes)
Speed-up ratio (compared to unparalleled version)
4. Patterns and Explanations

4.1. Fix #2 performance pattern

Pattern: Fix #2 performance pattern is independent of padding size and shows clear speed-up ratios respective to the number of threads used.

Explanation: This is because it doesn’t use padding as its remedy to fix the cache false sharing issue. Instead, it fix the issue by reduce the number of direct read-write operations from/to cache line in each thread by using private variable (in this case is tmp). Thus, for each thread, there are only 1 direct read and 1 direct write from/to the cache line; and therefore, the cache line didn’t have to be reloaded/revalidated repeatedly from memory which make the performance much better than fix #1 (when the padding size isn’t large enough yet) or unfixed version.

4.2. Fix #1 performance pattern

(1) Pattern: At the padding size of 0, Fix #1-2 threads and Fix #1-4 threads is just as good as the performance baseline for 1-thread (unparalleled).
Explanation: Because there’s no padding, all threads read and write directly from/to the same cache line constantly, which makes the cache being reloaded/revalidated constantly from memory and thus suffer from the added latency for data to constantly move between CPU and memory and constantly make the computation (of CPU) wait for those latency. These negative effect of false-sharing is so much in this case that it out weights the benefit of both 2-threads and 4-threads parallelization, making their performance being just as good as the performance of 1-thread (unparalleled)

(2) Pattern: Starting at the padding size of 3 and padding size of 7, Fix #1-2 threads and Fix #1-4 threads, respectively, starts performing as good as the performance baseline for 2 threads. Starting at padding size of 13, Fix #1-4 threads’ starts performing as good as the performance baseline for 4 threads from then on.
Explanation: Continue from the explanation of pattern (1), now as the padding size increases larger and larger, the threads experience less and less false sharing, which make their performance (or speed-up ratio) go up. Once the Fix#1-2 threads no longer experience false sharing, it performance as expected – as good as the performance baseline for 2 threads from then on. However, the Fix#1-4 threads still experience this issue since there are more threads thus the large enough padding size thresholds to eliminate the false-sharing is higher, which is in this case is padding size of 13 (of 4 bytes unit).

- (3) Pattern: The milestones of padding size of 3, 7, and 13 are several units smaller than those milestones expected in the lecture notes.
- Explanation: A possible explanation for this pattern is because my program didn’t allocate the array element at the beginning of the cache line but a little off to the right. Thus, it takes smaller padding sizes for the data to be pushed and spread onto the other cache lines; and so the threshold is smaller than the case in which the first element of array is allocated at the beginning of the cache line